## LAB ASSIGNMENT 1 - Installing Network Hardware

Materials Needed:

- Computer

- Network card

- Piece of  UTP cable

- Two RJ45 terminals

- Wire strippers

- Wire crimpers

Activity

You and your partner(s) have just been hired by the FishNet Computer Company. If you have installed a network card, you may NOT touch the computer or card. You are to supervise and offer advice to your partners. Your first assignment is to install a network on the computers in the Lab. You will need to:

- Build a unshielded twisted-pair (UTP) network cable.

- Cut the end of the cable to the desired length

- Strip the cable

- Arrange the wires so that they lay flat in the proper sequence

- Insert the wires in the correct pin channels

| Pin Number | Proper Connection |
| --- | --- |
| Pin 1 | Orange/white wire |
| Pin 2 | Orange wire |
| Pin 3 | Green/white wire |
| Pin 4 | Blue wire |
| Pin 5 | Blue/white wire |
| Pin 6 | Green wire |
| Pin 7 | Brown/white wire |
| Pin 8 | Brown wire |

- Crimp the wires

- install one of the provided network adapter cards (located next to your computer) in one of the computers that does not have a network card already installed.

- connect the computer to the LAN using the cables, terminators and Ts provided. If the card you install is a combo card (has an RJ45 connection), connect the computer to the network using UTP.

- install the correct drivers for the network adapter card from Windows or the disk(s) provided.